## Slide 1: “Underwater applications of the Ambisonics technology”
Author: Angelo Farina – HTTP://www.angelofarina.it
E-mail: farina@unipr.it – Skype: angelo.farina
University of Parma
Industrial Engineering Department
HTTP://ied.unipr.it

## Slide 2: Goals
Explanation of the Ambisonics technology, as currently employed in room acoustics
Brahma: the first underwater 4-channels digital sound recorder
A tetrahedrical hydrophone array for Brahma
Sound source localization from Ambisonics (B-format) recordings
Noise immission mapping employing a modified version of the CITYMAP computer program

## Slide 3: Ambisonics technology
Ambisonics was invented in the seventies by Michael Gerzon (UK)
It was initially a method for recording a 4-channel stream, which later was played back inside a special loudspeaker rig
It is based on the pressure-velocity decomposition of the sound field at a point
It makes it possible to capture the complete three-dimensional sound field, and to reproduce it quite faithfully

## Slide 4: Ambisonics recording and playback
Reproduction occurs over an array of 8-24 loudspeakers, through an Ambisonics decoder

## Slide 5: Ambisonics Technology
Recording
Processing
Playback
Encoding
B-Format
Decoding
Speaker-feeds
Notes: Ambisonic surround sound è un set di tecniche per la registrazione, l’elaborazione in studio e la riproduzione dell’intero campo sonoro incontrato durante la ripresa. La modalità con cui Ambisonic realizza la più fedele riproduzione possibile consiste nel progettare tutta la catena di passaggi che dalla ripresa dell’evento sonoro lo portano fino alle orecchie degli ascoltatori. Attraverso un processo di codifica, un definito set di segnali chiamato B-Format ed un processo di decodifica, riesce ad ottenere un ambiente di riproduzione, in cui lo spettatore ha più ampia libertà di movimento all’interno dell’area d’ascolto senza correre il rischio di compromettere l’immagine sonora.

## Slide 6: The Soundfield microphone
This microphone is equipped with 4 subcardioid capsules, placed on the faces of a thetraedron
The signal are analogically processed in its own special control box, which derives 4 “B-format” signals
These signals are:
  W : omnidirectional (sound pressure)
  X,Y,Z : the three figure-of-eight microphones aligned with the ISO cartesian reference system – these signals are the cartesian components of the “particle velocity” vector

## Slide 7: Other tetrahedrical microphones
Trinnov, DPA, CoreSound, Brahma are other microphone systems which record natively the A-format signals, which later are digitally converted to B-format

## Slide 8: The B-format components
Physically, W is a signal proportional to the pressure, XYZ are signals proportional to the three Cartesian components of the particle velocity
when a sound wave impinges over the microphone from the “negative” direction of the x-axis, the signal on the X output will have polarity reversed with respect to the W signal

## Slide 9: A-format to B-format
The A-format signals are the “raw” signals coming from the 4 capsules, loated at 4 of the 8 vertexes of a cube, typically at locations FLU-FRD-BLD-BRU

## Slide 10: A-format to B-format
The A-format signals are converted to the B-format signals by matrixing:
W' = FLU+FRD+BLD+BRU
X' = FLU+FRD-BLD-BRU
Y' = FLU-FRD+BLD-BRU
Z' = FLU-FRD-BLD+BRU
and then applying proper filtering:

## Slide 11: Recording
X
Y
Z
W
Directional components: velocity
Omnidirectional component: pressure
Soundfield Microphone
Polar Diagram
B-FORMAT
Recording
Encoding
Processing
Decoding and Playback
Notes: Il soundfield è un microfono che include nella sua struttura un array di quattro capsule che catturano il suono in tre dimenzioni senza presentare errori di fase e formano il diagramma polare caratteristico. Effettuando una registrazione con il soundfiled si ottengono in output 4 segnali audio: 3 componenti direzionali contenenti informazioni sulla la velocità del suono lungo gli assi
X
Y
Z
ed una componente omnidirezionale che da informazioni sulla pressione sonora.
L’insieme delle quattro componenti audio costituisce il set di segnali di codifica della tecnologia Ambisonic chiamato B-Format.
E’evidente che se la registrazione è fatta con il soundfield non occorrono processi di codifica.

## Slide 12: Encoding (synthetic B-format)
Recording
Encoding
Processing
0 | W | 
1 | X | 
 | Y | 
 | Z | 
=0,707
=cos(A)cos(E)
=sin(A)cos(E)
s(t)=
=sin(E)
*s(t)
*s(t)
*s(t)
*s(t)
Decoding and Playback
Notes: Nel processo di codifica, implementato da Isaac e me su DSP, vengono assegnate delle coordinate spaziali a sorgenti mono tramite un set di quattro equazioni.
L’algoritmo matematico, proposto da Gerzon, che porta alle equazioni, scinde la direzione del campo sonoro in componenti armoniche sferiche di ordine zero ed uno. Ponendo l’ascoltatore nell’origine degli assi, tutti gli eventi acustici possono essere rappresentati da quattro componenti fondamentali:
W
X
Y
Z
Dove A ed E sono rispettivamente gli angoli di Azimuth (rotazione antioraria rispetto ad un asse di riferimento) ed Elevation (angolo di elevazione).
Moltiplicando l’ampiezza variabile nel tempo della sorgente sonora per i coefficienti dati dalle armoniche sferiche, la si dispone sulla superficie della sfera unitaria data da:
EQUAZIONE
che circonda l’ascoltatore.
W, X, Y, Z diventano così la codifica B-Format di s(t).

## Slide 13: Processing
Rotation
Tilt
Tumble
Recording
Encoding
Processing
Decoding and Playback
Notes: Una volta ottenuto il B-Format, è possibile intervenire su di esso per cambiare la direzione del compo sonoro senza ricodificare tutte le sorgenti:

## Slide 14: Decoding & Playback
Each speaker feed is simply a weighted sum of the 4 B-format signals.
The weighting coefficients are computed by the cosines of the angles between the loudspeaker and the three Cartesian axes
Recording
Encoding
Processing
Decoding and Playback

## Slide 15: Software for Ambisonics decoding
Audiomulch VST host
Gerzonic bPlayer
Gerzonic Emigrator

## Slide 16: Software for Ambisonics processing
Visual Virtual Microphone by David McGriffy (freeware)

## Slide 17: Rooms for Ambisonics playback
University of Bologna
University of Ferrara
ASK (UNIPR) – Reggio Emilia

## Slide 18: Rooms for Ambisonics playback
University of Parma (Casa della Musica)

## Slide 19: BRAHMA: 4-channels recorder
A Zoom H2 digital sound recorder is modified in India, allowing 4 independent inputs with phantom power supply

## Slide 20: BRAHMA: 4-channels recorder
The standard microphone system is usually a terahedrical probe equipped with 4 cardioid electrect microphones

## Slide 21: Hydrophones for Brahma
Brahma provides phantom power (5V) for transducers equipped with integral electronics. Hence the ideal hydrophone is the Acquarian Audio H2A:
Aquarian Audio Products
A division of AFAB Enterprises
1004 Commercial Ave. #225 Anacortes, WA 98221 USA
(360) 299-0372 www.AquarianAudio.com

## Slide 22: Underwater probe for Brahma
For underwater recordings, a special setup of 4 screw-mounted hydrophones is available:

## Slide 23: Underwater case for Brahma
Due to the small size (like a cigarette packet) it is easy to insert the Brahma inside a waterproof cylindrical container, sealed with O-rings
An external lead-acid battery can be included for continuous operation up to one week (in level-activated recording mode)
cable
6V 12 Ah battery

## Slide 24: BRAHMA: 4-channels recorder
The probe can be mounted on a weighted base, allowing for underwater placement of the recorded, inside a waterproof case. However, the cables are long enough (15m) also for keeping the recorder on the boat

## Slide 25: BRAHMA: 4-channels underwater recorder
The system is aligned vertically by means of a bubble scope, and horizontally by means of a magnetic compass:

## Slide 26: BRAHMA: 4-channels underwater recorder
Once placed on the sea bed, the system is usually well accepted (and ignored) by the marine life:

## Slide 27: Brahmavolver: the processing software
Brahma records A-format signals. They can be converted to standard B-format by means of the Brahmavolver program, running on Linux / Windows / Mac-OSX

## Slide 28: BRAHMA: technical specs
Sampling rates: 44.1 kHz, 48 kHz, 96 kHz (2 ch. only)
Recording format: 1 or 2 stereo WAV files on SD card
Bit Resolution: 16 or 24 bits
3 fixed gain settings, with 20 dB steps (traceable)
Memory usage: 1.9 Gbytes/h (@ 44.1 kHz, 24 bits, 4 ch.)
Recording time: more than 16 hours (with 32 Gb SD card)
Power Supply: 6 V DC, 200 mA max
Automatic recording when programmable threshold is exceeded
The SD card can be read and erased through the USB port

## Slide 29: Source localization from B-format signals
At every instant, the source position is known in spherical coordinates by analyzing the B-format signal
a = azimuth - q = elevation
x
y
z
buoy
Tetrahedrical hydrophonic probe
boat
a
q

## Slide 30: Trajectory from multiple recording buoys
Employing several buoys, the complete trajectory can be triangulated

## Slide 31: Underwater extension of Citymap
If Citymap is to be employed for underwater applications, two main modifications are required:
  A new data-base of marine noise sources needs to be compiled
  The propagation algorithm must be replaced with a more realistic one, which takes into account the inhomogeneous medium and the multiple reflections between sea surface and sea floor.
The first task is accomplished by performing thousands of recording of pass-by recordings with various types of boats, at various speeds, and with different sea state
The second task requires a substantial effort for the software developer, who will have to rewrite completely the subroutine which performs the computations

## Slide 32: Example of usage of Underwater Citymap
Mapping of underwater sound pressure level due to a boat along a trajectory

## Slide 33
Internet resources
All the papers previously published by Angelo Farina can be downloaded from his personal web site:
www.angelofarina.it
The CITYMAP program can be downloaded from:
www.angelofarina.it/Public/Disia
Its use is free for academic research in public institutions (password issued on request)